## Slide 1
Core scheduling: for SMT security and performance
Aubrey Li @ CLK2019
Intel Open Source Technology Center

## Slide 2
Agenda
SMT Security
SMT Performance
Core scheduling
Future work

## Slide 3
A roast on Linux Plumber Conference 2019

## Slide 4
Security Issue: Side-channel Attack Example
L1 Terminal Fault(L1TF) Vulnerability
    Exploit speculative execution to ignore the non-present page table entry (PTE) and load the referenced data if it is present in the Level 1 data cache
    Mitigation
      Host
        PTE Inversion
        Interrupt affinity
        SMT off
      Guest
        L1D cache flush on privilege boundaries (VMENTER)
        Guest VCPU confinement to dedicated physical cores
        Disable extended page table (EPT)
Task isolation
cache
CPU Core
SMT0
SMT1

## Slide 5
Performance Issue: Fast Instructions Go Slow
AVX512 instructions accelerate performance of demanding computational tasks up to 40% (vs AVX2)
    Linpack, FPU Julia, etc
AVX512 pulls down the core max frequency
      Good Case
      Bad Case
NonAVX
AVX
NonAVX
AVX
Freq = 3.5GHz
Freq = 3.5GHz
Core0
Core1
AVX
AVX
NonAVX
NonAVX
Freq = 3.5GHz
Freq = 3.8GHz
Core0
Core1
5

## Slide 6
Mitigate Frequency Reduction
AVX512 task detection
    Performance monitoring event
      core_power.lvl2_turbo_license
    sysfs interface
      cat /proc/<pid>/arch_status
      AVX512_elapsed_ms: 12
    cgroup interface for orchestration (TBD)
      cat /sys/fs/cgroup/cpuacct/cpuacct.arch_status
      AVX512_elapsed_ms: 12
AVX512 task isolation
6

## Slide 7
CPU Scheduling
Core Scheduling
Core0
Core1
Core2
Core0
Core1
Core2
Per thread scheduling
    Each thread selects task from its own runqueue
    Load balance keeps runqueue balanced
Per core scheduling
    All SMTs in a core select tasks together
    scheduling for a core is synchronized
7

## Slide 8
Core Scheduling Design
Make SMT usable on systems with L1TF
Have a core wide knowledge to schedule tasks on SMT instances
    Core Cookie
    Per-core run queue (and lock)
Force a sibling idle if no matched task found in the same core
    resched IPI ensures no overlap
Core0
SMT0
SMT1
Idle
SMT2
SMT3
Core1
AVX
Idle
Non-AVX
Core0
SMT0
SMT1
AVX
SMT2
SMT3
Core1
AVX
8

## Slide 9
Current Linux Scheduler Overview
CPU0
  rq->cfs_rq->
  task_timeline.rb_tree
virtual runtime
CPU1
  rq->cfs_rq->
  task_timeline.rb_tree
virtual runtime
load balance
wait queue
sleep
wakeup
sleep
wakeup
sched_entity
9

## Slide 10
Upstream Proposal – Core Scheduling
CPU0
  rq->cfs_rq->
  task_timeline.rb_tree
    core_cookie
    core_tree.rb_tree
virtual runtime
CPU1
  rq->cfs_rq->
  task_timeline.rb_tree
    core_cookie
    core_tree.rb_tree
virtual runtime
load balance
wait queue
sleep
wakeup
sleep
wakeup
sched_entity
task priority
10

## Slide 11
Core Scheduling Current Status
V3 posted
    Initiated by Peter Zijlstra(V1)
    Build and stability fixes(V2)
    Bug fixes and Performance optimization(V3)
It will eventually be merged, for:
    Security(L1TF, MDS)
    Performance(Workload colocation)
    Real time
    etc
11

## Slide 12
Performance Result
sysbench CPU + Gemmbench
Core scheduling shows 10%~20% improvement against default case
Chart: Sysbench CPU + Gemmbench
Default | 26859.815 | 32285.8702 | 36874.3362 | 38581.5597
CoreSched | 29764.3705 | 38551.9922 | 40749.0519 | 42283.3095
NoSMT | 25400.676 | 26463.7649 | 25703.6733 | 27237.1613
CoreSched% | 10.8138 | 19.4082 | 10.5079 | 9.5946
Chart: CPU Utilization
Default | 60.11 | 89.26 | 97.69 | 100
CoreSched | 59.73 | 88.93 | 96.22 | 97.4
NoSMT | 97.69 | 99.51 | 100 | 100
12

## Slide 13
Performance Result
sysbench mysql + Gemmbench
Core scheduling shows 60% improvement at mid load case but -80% regression at overload case
Chart: Sysbench MySQL+ Gemmbench
Default | 9188.3407 | 16610.1216 | 17106.318 | 15090.6343
CoreSched | 15820.0383 | 16863.2938 | 12556.1082 | 3015.0942
NoSMT | 9334.2438 | 12715.2398 | 17118.0112 | 18859.5333
CoreSched% | 72.1751 | 1.5242 | -26.5996 | -80.0201
Chart: CPU Utilization
Default | 60.14 | 89.27 | 97.82 | 99.52
CoreSched | 61.77 | 88.79 | 94.52 | 95.88
NoSMT | 96.66 | 99.28 | 99.94 | 100
13

## Slide 14
Future Work - Security
User to Kernel Attack Isolation
    Interrupt
    Syscall
    VMEXIT
Guest OS0
VM0
App
App
…
VM Monitor
VM exit
Guest OS1
VM1
App
App
…
SMT0
SMT1
L1 Cache
14

## Slide 15
Future Work - Performance
Fairness
Task placement
Performance regression
Chart: sysbench mysql throughput
15